## Slide 1: CHAP I. Introduction
Numerical Simulation
of
Turbulent Flows - LES

## Slide 2: Turbulence
I. Introduction
Laminar Flow
Turbulent Flow

## Slide 3: Techniques for Turbulence Simulation
I. Introduction
  Governing Equations of Fluid Mechanics
  Mass conservation
  Momentum conservation
  Species transport
  Energy conservation
Navier-Stokes equations
Scalar transport equations
  Turbulence information
  The non-linear governing PDEs contains the whole information on turbulent fields.
  Accept solutions fluctuating over a wide range of scales when some parameters (e.g. Re number) exceeds a threshold.

## Slide 4: Techniques for Turbulence Simulation
I. Introduction
  DNS (Direct Numerical Simulations)
  No modeling
  Resolution of all scales
  Prohibitive computational costs
  Moderate Re number and simple geometries

## Slide 5: Techniques for Turbulence Simulation
I. Introduction
  Filtering (LES) and Averaging (RANS)
  Removing high frequency fluctuations
Experiment
LES
RANS
  Turbulent
  Flame

## Slide 6: Techniques for Turbulence Simulation
I. Introduction
  Filtering and Averaging
  Physical space

## Slide 7: Techniques for Turbulence Simulation
I. Introduction
  Filtering and Averaging
  Spectral space

## Slide 8: Techniques for Turbulence Simulation
I. Introduction
  Closure problem (origin)
Averaging
Filtering
  + non-linearity
  = closure problem

## Slide 9
  Mass:
  Momentum (i =1, 2, 3):
  Species (N species with k=1,..,N):
  Total enthalpy (ht = h + uiui/2):
Techniques for Turbulence Simulation
I. Introduction
  Closure problem (governing equations)
Reynolds stresses

## Slide 10: Techniques for Turbulence Simulation
I. Introduction
  Closure problem (modeling)
  RANS (Reynolds-Averaged Navier-Stokes equations) [stationary]
    Eddy-viscosity models (Gradient diffusion assumption)
      Zero-equation models
      One-equation models
      Two-equation models (k-ε, k-ω, …)
      Three-equation models
      Four-equation models (v2-f)
      Non-linear models
    RSM (Reynolds Stress (transport) Model)
  LES (Large Eddy Simulation) [stationary and instationary]
  PDF (Probability Density Function) [combustion]

## Slide 11: Techniques for Turbulence Simulation
I. Introduction
  Closure problem (modeling)
  RANS
  LES
  PDF
DES (Detached Eddy Simulation)
FDF (Filtered Density Function)

## Slide 12: Current state of LES simulations
I. Introduction
  From homogeneous shear flows
  To multi-phase flow combustion in complex geometries

## Slide 13: Course Outline
I. Introduction
  Turbulence
  Governing Equations (Chap II)
  Mathematical tools for studying turbulence
    Statistical (Chap III) versus deterministic
    Physical space (Chap V) versus spectral space (Chap VI)
  Turbulence Simulation
  Overview of different models, esp. RANS (Chap VII)
  LES (Chap VIII)
  Introduction to PDF (Chap IX) *